## Slide 1: An Intro to Internet Protocol version 6
IPv6
Joe James

## Slide 2: Background
Internet Protocol (IP) is the primary protocol in the Internet layer of the OSI networking model
IP’s job is to deliver packets from a source computer to a destination computer based on the IP addresses in the packet headers
As of May 2015, about 97% of web traffic uses IPv4
IPv6 is intended to eventually replace IPv4

## Slide 3: Why IPv6?
By the late 1980s, it was obvious that IPv4 addresses would need to be conserved
By the early 1990s, it became clear that IPv4’s addressing was inadequate, even with conservation methods
In early 1992, several proposals for a new Internet addressing system were published

## Slide 4: Why IPv6?
IPv4 address exhaustion is the main reason:
  IPv4 only supports 4.3 billion addresses
  IPv4 address space is poorly allocated, with only 14% of all available addresses in use

## Slide 5: Number of devices in use today
Automobiles: 1.1 Billion
Smart Phones: 1.8 Billion
Web sites: 650 Million
Televisions: Yikes!
Security Cameras: Double Yikes!!

## Slide 6: IPv6 Overview
2001:db8::42:c857:2e:65:7334
Leading zeros can be omitted.
All-zero groups can be omitted.
IPv6 addresses are represented as eight groups of four hexadecimal digits separated by colons
IPv6 is an Internet Layer protocol for packet-switched internetworking and provides end-to-end datagram transmission across multiple IP networks
Notes: See my notes here.

## Slide 7: IPv4 vs IPv6
 | IPv4 | IPv6
Deployed | 1981 | 1999
Address Size | 32-bits | 128-bits
Address Format | Dotted Decimal: 192.168.27.134 | Hex: 3FFE:F200:234:AB00: 123:4567:8901:ABCD
Number of Addresses | 232 = 4,294,967,296 | 2128 = 340,282,366,920,938,463, 463,374,607,431,768,211,456
Addressing | Class-based | Classless

## Slide 8: Factors Speeding and Slowing Exhaustion of IPv4 Addresses
Accelerating Exhaustion
Rapid growth of number of internet users
Fast growth of mobile devices
Always-on devices (eg. DSL)
Poor allocation of addresses
Slowing Exhaustion
Subnetting / CIDR
Network address translation (NAT / PAT)
Use of private networks
DHCP

## Slide 9: More Address Space
The main advantage of IPv6 over IPv4 is its larger address space. IPv6 offers 2128 (or about 3.4×1038) addresses
That is over 7.9×1028 times more than IPv4, which uses 32-bit addresses
IPv6 provides about 5×1028 addresses for each of the seven billion people alive in 2014

## Slide 10: IPv6 Packet Header
Cleaner packet header enables more efficient processing by routers
Rarely used and optional fields either removed or moved to separate optional header extensions

## Slide 11: IPv6 Packet Header
The header is the first 40 Bytes of the IPv6 packet, with minimal functionality required for all packets
32 of those 40 Bytes are source and destination addresses

## Slide 12: IPv4
IPv6

## Slide 13: IPv4
IPv6

## Slide 14: IPv4
IPv6

## Slide 15: IPv4
IPv6

## Slide 16: IPv4
IPv6

## Slide 17: IPv4
IPv6

## Slide 18: IPv4
IPv6

## Slide 19: IPv4
IPv6

## Slide 20: IPv4
IPv6

## Slide 21: IPv4
IPv6

## Slide 22: IPv4
IPv6

## Slide 23: IPv4
IPv6

## Slide 24: IPv4
IPv6

## Slide 25: IP6 Packet Header
Deleted Fields:
Fragmentation fields moved out of standard header
Options moved from header into payload
Header Checksum eliminated
Header Length field eliminated (fixed at 40B)
Length field excludes IPv6 header

## Slide 26: IP6 Packet Header
Revised Fields
Time to Live => Hop Limit
Protocol => Next Header
Type of Service => Traffic Class
Address size increased 32 bits => 128 bits
New Flow Label field added

## Slide 27: Goodbye Broadcast, Hello Anycast!
Unicast
Multicast
Broadcast
Unicast
Multicast
Anycast
Broadcast replaced by expanded use of Multicast
New Anycast ideal for connecting to a wifi
IPv4
IPv6

## Slide 28: IPv6 New Features
Stateless Auto-configuration
  New host can assign its own host address
  No need for DHCP
Supports new IP security protocols
  Authentication of source
  Encryption of payload
IPv4 and IPv6 packets both limit payload size to 64KB. However, with a Jumbo Payload option, the IPv6 may have up to 4GB payload

## Slide 29: IPv4 to IPv6 Translation
IPv6 is not backward compatible with IPv4. IPv6 is a parallel, independent network.
IPv4 will co-exist with IPv6 for the foreseeable future
Exchanging traffic between the two networks requires translator gateways using NAT64

## Slide 30
- John Chambers,
President and CEO of Cisco Systems
“If we don't overcome the challenges of IPv4 we will slow down the growth of the Internet and lose momentum as an industry. IPv6 is important to all of us, to everyone around the world. It is crucial to our ability to tie together everyone and every device. “